## Slide 1: Ensuring Home-based Rehabilitation Exercise by Using Kinect and Fuzzified Dynamic Time Warping Algorithm
Qiao Zhang

## Slide 2: Outline
Concept Introduction
Background and Motivation
Related Work
Research Methodology
Implementation
Conclusion

## Slide 3: Concept Introduction

## Slide 4: Rehabilitation
Treatments and exercises concerned with remediation of impairments and disabilities.
Notes: When physicians evaluate trajectory and speed of rehabilitation exercise mainly based on their experience and subjective evaluation without utilizing more precise and measurable computer value.

## Slide 5: Fuzzy Logic
In contrast with traditional logic theory, where traditional binary sets have two-valued logic: true or false, fuzzy logic variables may have a truth value that ranges between 0 and 1.
Notes: When physicians evaluate trajectory and speed of rehabilitation exercise mainly based on their experience and subjective evaluation without utilizing more precise and measurable computer value.

## Slide 6: Background and Motivation

## Slide 7: Rehabilitation
In the case of rehabilitation, a traditional therapy process generally conducted in a hospital setting and requires direct supervision of a skilled caregiver. The aim of home-based rehabilitation is to provide an in-home alternative to in hospital rehabilitation. Home-based rehabilitation allows for great flexibility so that patients can tailor their program of rehabilitation and conform to individual schedules.

## Slide 8: Kinect
Preprocessing that detects human object silhouette and extracts silhouette descriptors
Pose estimation that quantitatively characterizes and localizes human limbs in each frame.

## Slide 9: Dynamic Time Warping Algorithm
In time series analysis, dynamic time warping (DTW) is an algorithm for measuring similarity between two temporal sequences which may vary in time or speed.
They utilize the benefit of DTW algorithm to solve comparing two sequences which have different time length in order to determine the similarity between the standard and the patient exercise.
Notes: Euclidean distance measurement between frames is generally unsuitable for comparing two sequential movements which have different time lengths because it is sensitive to even a small distortion in time axis. For instance, similarities in walking patterns could be detected using DTW, even if one person was walking faster than the other, or if there were accelerations and decelerations during the course of an observation.

## Slide 10: Fuzzy Logic
When physicians evaluate trajectory and speed of rehabilitation exercise mainly based on their experience and subjective evaluation without utilizing more precise and measurable computer value.
Therefore, they cannot set a value of trajectory and speed to evaluate result using traditional logic theory.

## Slide 11: Related Work

## Slide 12: Rehabilitation with Device Help
Many researches use industrial motion sensors and Nintendo Wii Remote to assist physicians and patients.
(x) Uncomfortable and boring: motion sensors have some defects, such as patients need to fasten it on limbs, hold it in the hands or wear it on the body.

## Slide 13: Kinect Applications
These Kinect games can let users to do exercise in their home, but the wrong exercise leads to sports injuries.
Previous work proved that patients can get more motivation and outcome of rehabilitation with Kinect. But their rehabilitation systems are too specific.

## Slide 14: Fuzzy Logic
There are a handful of existing systems that utilize fuzzy logic evaluation.
The accuracy can be as high as 80-90%.
Further, the application of fuzzy set theory can provide an effective way to formulate decision problems in a fuzzy environment where the information available is subjective and imprecise.

## Slide 15: Research Methodology

## Slide 16: Phases
A tailored exercise is performed by the patient and recorded under the supervision of a physician by using the proposed KEHR system.
The evaluation can then be achieved by exploring the differences derived from two factors: 1. Trajectory disparity: the motional path created by each joint over time 2. Speed variation: the time consumption in completing a designated exercise.

## Slide 17: The KEHR Architecture
Notes: The Kinect-based rehabilitation management module provides full functionality for users to practice rehabilitation exercise with Kinect at home.
The Data Repositories module Exercise Database and User Profile.

## Slide 18: Kinect-based Rehabilitation Management Module
Manage rehabilitation process
Capture user performed exercise under supervision of a professional
Replay the exercise for user to execute at home
Evaluate the performance of the exercise.

## Slide 19: Capture
Notes: An example of captured positional data of “Hand_right” and “Hand_left” joints is illustrated in this table.

## Slide 20: Evaluate - Overview
Notes: This is the core function in KEHR system. This function applies the DTW algorithm that can adapt to sequences that vary in speed and time for measuring the similarity of streaming joint data between “at-home” and “in-hospital” videos. The sequence of captured joint data (at-home data) will then be used to compare against the sequence stored (in-hospital data) in the data repository.

## Slide 21: Evaluate - DTW
Given two time series A = (a1, a2, … , am) and B = (b1, b2 , … , bn) where ai = ( xi, yi, zi ), i=1,…,m; bj = ( xj , yj , zj ), j=1,…,n; To align two sequences using DTW they construct an n-by-m matrix where the (ith, jth) element of the matrix contains the Euclidean distance between the two points ai and bj.
A warping path P is a contiguous set of matrix elements that defines a mapping between A and B. The warping path has too satisfy 3 criteria: Boundary condition, Continuity, Monotonic condition
Notes: This is the core function in KEHR system. This function applies the DTW algorithm that can adapt to sequences that vary in speed and time for measuring the similarity of streaming joint data between “at-home” and “in-hospital” videos. The sequence of captured joint data (at-home data) will then be used to compare against the sequence stored (in-hospital data) in the data repository.

## Slide 22: Evaluate – DTW example
Notes: This is the core function in KEHR system. This function applies the DTW algorithm that can adapt to sequences that vary in speed and time for measuring the similarity of streaming joint data between “at-home” and “in-hospital” videos. The sequence of captured joint data (at-home data) will then be used to compare against the sequence stored (in-hospital data) in the data repository.

## Slide 23: Evaluate – DTW example
Notes: This is the core function in KEHR system. This function applies the DTW algorithm that can adapt to sequences that vary in speed and time for measuring the similarity of streaming joint data between “at-home” and “in-hospital” videos. The sequence of captured joint data (at-home data) will then be used to compare against the sequence stored (in-hospital data) in the data repository.

## Slide 24: Evaluate – DTW example
Notes: This is the core function in KEHR system. This function applies the DTW algorithm that can adapt to sequences that vary in speed and time for measuring the similarity of streaming joint data between “at-home” and “in-hospital” videos. The sequence of captured joint data (at-home data) will then be used to compare against the sequence stored (in-hospital data) in the data repository.

## Slide 25: But what is DTW distance?

## Slide 26: Evaluate – DTW example {(a6,b5) (a5,b5) (a4,b4) (a3,b3) (a2,b2) (a1,b1)}
Notes: This is the core function in KEHR system. This function applies the DTW algorithm that can adapt to sequences that vary in speed and time for measuring the similarity of streaming joint data between “at-home” and “in-hospital” videos. The sequence of captured joint data (at-home data) will then be used to compare against the sequence stored (in-hospital data) in the data repository.

## Slide 27: Evaluate - Fuzzy Inference
The Euclidean distance Ed of the optimal path is calculated for serving as a metric of disparity between A and B.

## Slide 30: Implementation

## Slide 33: Conclusion

## Slide 34: Conclusion
They tested the KEHR on three different shoulder rehabilitation exercises performed by four different users. The evaluation by KEHR agrees with the physician with the average of 80.01%. This result shows that KEHR is suitable for home-based rehabilitation exercise.

## Slide 36: Using the Kinect to Encourage Older Adults to Exercise

## Slide 37: Motivation
Though older adults are willing to exercise, they fear injury, which is a hindrance. They would prefer exercising at their convenience in the safety of their homes and to use methods that are cost-effective and convenient to them.
Make exercise fun, such as through a game.

## Slide 38: Data Gathering
Discussion with Field Expert The prime problem areas were identified as: (a) flexibility, (b) strengthening, (c) walking, and (d) balance.
Focus Group The discussion revealed that all of the participants walked on a regular basis and enjoyed the activity and saw it as pleasurable. However, they were also intimidated to take a walk by themselves because of safety issues.

## Slide 39: Design and Prototype

## Slide 40: Questions?
Thanks for listening!