## Slide 1: IoT systems view
Daniel mosse

## Slide 2: IoT bottom layer
Sensors at the bottom layer, collect data
  Sensors can be the few-cent sensor, bought in bulk for adding to a board or a sensor bundle that comes with a microcontroller already on board
  Sensor data usually is analog, requiring an ADC (analog to digital converter), which typically comes in sensor bundles
Sensor data can be processed locally
  To save bandwidth and energy, typical local data treatments include
    Suppression of duplicates
    Packing of multiple data items into a single message
  Depending on microcontroller, more sophisticated local treatment can be done
Sensor data is transmitted typically wirelessly (see protocol stack below)
  Like ADCs, the radio is typically present in sensor bundles
  There are many different options for hardware radios and protocols (e.g., Bluetooth, BLE—Bluetooth low energy, LoRa, Wi-Fi, …)

## Slide 3: IoT middle layer
Sensors (or bundles) send data
Router or gateway collects data from multiple sensors
The gateway is typically more powerful
  Several radios (collect sensor data wirelessly)
  More powerful CPU
  Added security
  Transmit data wired fashion
Is the gateway part of Edge Computing?
  Depends on definition

## Slide 4: IoT top layer
Gateway/Edge send data to Cloud servers
  Gateway can filter, treat, analyze data
  Typically use a publisher subscriber (pub-sub) model
    Many different examples and implementations, like MQTT
    Each cloud provider has its own
Cloud services are abundant
  “Free” or paid, or in between
  Can you trust servers with your data?
  Multiple gateways send data from multiple users
  Analyses are more powerful with more data and more servers (which also have more capabilities/ libraries)

## Slide 5: IoT system characteristics
Real time
  Some data items have a freshness period (deadline)
  Some actuation commands have a zero value (example?) or negative value (example) after a deadline
Access to devices
  One way (send data only) communication is more secure
  Two way (send data; receive data and commands) communication allows for
    Pros: OTA (over the air) updates, reconfiguration of devices, …
    Cons: security problems (reconfiguration of devices, malicious actuation)
Discovery of the devices
  To access a device, need:
    what the device is
    how to communicate with it
  Make it public or keep it private (what are the pros and cons?)

## Slide 6: More IoT system characteristics
Hardware is composed of: sensors, CPU, memory, network, specialized units, depending upon sensors (e.g., audio chip, video hardware, etc)
Developing applications requires a toolchain
  Vendor specific or open source
  IDE typically includes compiler, system analyzer (CPU/memory usage, timing diagrams, etc.)
  Scheduler can be downloaded with Application
“Applications” can be user level or middleware/libraries

## Slide 7: Other considerations
Operating system:
  Concurrency or not
  Instrumentation: different levels, Interface to turn it on or off, overhead considerations
  Allows for blocking devices, polling devices, or both
  Consider the network and protocol stack
Licensing requirements
  Software license
  Ownership of data
Privacy

## Slide 8: Protocol Stack
Internet examples
XML
HTTP
TLS
TCP
IPv6
IoT example equivalents
Web Objects
CoAP
DTLS
UDP
LoWPAN

## Slide 9: Power management
Device duty cycle (i.e., turning the device on/off)
Periodicity of collecting or transmitting data
Data compression, packing, …
Data transformations:
  how aggressive
  Location (sensor, Gateway, edge)
  energy impact